Replicator / TDMF UNIX IP Release 2.7.4

AIX rootvg failover

Design Document

Date: January 6, 2014
Revision 1.2

Table of Contents

Revision History
Revision	Date	Comments	Written By
1	09/20/13	Initial document	Paul Cloutier
1.1	10/03/13	Update after coding complete	Paul Cloutier
1.2	06/01/14	Update	Paul Cloutier

# 1. Overview

The main aspect of the AIX boot drive failover is that the Source Server prepares the necessary information on its rootvg /etc directory, which is replicated to the Target Server. Among other things, the boot script rc.tcpip, which starts all the network services, is modified so that it will call one of our scripts (new) to reconfigure the target server network upon failover boot. In the final sequence of the failover, the target part of the failover script modifies the boot list to boot from the replicated drive, which contains the modified rc.tcpip that will call our script before starting network services.

NOTE: we support only a 1-to-1 DR configuration, not loopback.
2 scenarios:
1. We voluntarily initiate a failover from the source server to the target server
2. We lose the source server and must initiate the failover on the target server itself

# 2. Implementation

## 2.1 Network parameters

When replicating the rootvg of the source server to the target server, this one inherits from the network parameters of the source, which cannot be functional. Therefore, upon failover to the replicated rootvg on the target server, the network must be reconfigured. The following describes how this is implemented and automated.

After replicator installation, the user must execute a new Replicator command that will prompt to enter the target server tcpip / network parameters: dtc-target-netinfo. This should be done at the time when configuring the replication group for the rootvg replication, so that the information is there ahead of time and gets replicated to the target server immediately, in case the source server would be lost. This command, from the information given, will create the parameter file /etc/SFTKdtc_rootvg_failover_network_parms.txt, which will be read by the script SFTKdtc_AIX_failover_boot_network_reconfig.sh whose purpose it to reset the target network configuration at failover boot (i.e. when switching to the replicated rootvg) on the target. The info that the user must provide is that which is expected in smitty Basic Configuration menu, plus the Replicator group number used for replication of the rootvg and the network adapter identifier. The network parameters can normally be found in /smit.log of the target server, where you should look for the most recent mktcpip logged entry, for instance:

>> /usr/sbin/mktcpip -h'sjpwr7ded' -a'9.30.121.29' -m'255.255.255.0' -i'en0' -n'9.0.128.50' -d'svl.ibm.com' -g'9.30.121.1' -A'no' -t'N/A'

The information to provide to dtc-target-netinfo is:
  - Target server hostname
  - Target host IP address
  - Subnetmask
  - Network interface (e.g. en0)
  - NameServer IP address
  - Domain name (e.g. svl.ibm.com)
  - Default Gateway IP address
  - Cost for default route (-C arg to mktcpip, set to 0)
  - Do active dead gateway detection on default route? (-A arg to mktcpip, yes or no)
  - CableType (-t arg to mktcpip, can be N/A)
  - Network adapter (ex.: inet0)
  - Replication group number

- dtc-target-netinfo also copies our script SFTKdtc_AIX_failover_boot_network_reconfig.sh to /etc so that it be visible early at boot time.
- Then it also creates the marker file: /etc/SFTKdtc_call_mktcpip_at_boot for when the target will reboot from the replicated drive. Note: this file will be seen only at failover boot with the replicated rootvg, since it is replicated to the new target boot drive, not the original one. This flag file is deleted on the first failover boot, by our network reconfiguration script, so that this reconfiguration is done only once.
- At failover boot on the target (switching to replicated rootvg) the script /etc/SFTKdtc_AIX_failover_boot_network_reconfig.sh will reset the target server network configuration ONLY IF THE FLAG FILE /etc/SFTKdtc_call_mktcpip_at_boot exists and if the machine booting is the target machine, not the source machine.
- If the provided info passes validation and the target network parameter file is created, dtc-target-netinfo edits /etc/rc.tcpip to add a line at its start so that it will call our script : /etc/SFTKdtc_AIX_failover_boot_network_reconfig.sh.
- We must prevent the SOURCE server, if it reboots for some reason, to take this marker file /etc/SFTKdtc_call_mktcpip_at_boot as if were intended to itself, which could cause reconfiguring the SOURCE network as if it were the target. The current implemented way of handling this is by checking the bootlist: if we boot from the hdisk identified as the source rootvg hdisk in the Replicator configuration file and the SFTKdtc_services_disabled marker file is not found, it may be that we are on the SOURCE server and it was rebooted for some reason. If this is the case, i.e. no SFTKdtc_services_disabled flag found and booting from hdisk identified as the SOURCE rootvg hdisk, then we ignore the marker file /etc/SFTKdtc_call_mktcpip_at_boot if it is found.
Example of messages at the end of running dtc-target-netinfo, after having entered all the required input. The utility asks for confirmation that the input is correct. If the user does not confirm with yes (y), it prompts for the item number to change.

bash-3.2# dtc-target-netinfo
….
---------------------------------------------------------------------------------------
Please confirm that the input is correct:
     1) Target server hostname...................................... sjpwr7ded
     2) Target host IP address (ex: 1.2.3.4)........................ 9.30.121.29
     3) Subnetmask (ex: 255.255.255.0):............................. 255.255.255.0
     4) Network interface (ex: en0):................................ en0
     5) Name Server IP address...................................... 9.0.128.50
     6) Domain name (ex: subdomain.domain.com)...................... svl.ibm.com
     7) Default Gateway IP address.................................. 9.30.121.1
     8) Cost for default route (-C arg to mktcpip, ex: 0)........... 0
     9) Active dead gateway detection on default route? (yes/no).... no
    10) CableType (-t arg to mktcpip, dix/bnc or N/A)............... N/A
    11) Network adapter (ex.: inet0)................................ inet0
    12) TDMF UNIX Replicator group number........................... 0
---------------------------------------------------------------------------------------

  Are all these values correct [y/n]? y

The network configuration parameters have been saved in /etc/SFTKdtc_rootvg_failover_network_parms.txt.
These values will be used to configure the network when switching over to the replicated root drive on the target server sjpwr7ded.

Inserting call to SFTKdtc_AIX_failover_boot_network_reconfig.sh at line number 44 of /etc/rc.tcpip.

    Please inspect /etc/rc.tcpip

    the following lines have been added after start()

      # @@@ CALL TO SFTKdtc FAILOVER NETWORK RECONFIGURATION SCRIPT + @@@\
      /etc/SFTKdtc_AIX_failover_boot_network_reconfig.sh\
      # @@@ CALL TO SFTKdtc FAILOVER NETWORK RECONFIGURATION SCRIPT - @@@

## 2.2 Scenario 1: failover initiated voluntarily from the source server
- On the source server, we expect that we are in Normal mode after Full Refresh
- We give the command dtcfailover for the rootvg replication group: dtcfailover -g0 -b
- dtcfailover validates the configuration: only 1-to-1 is supported, not loopback
- dtcfailover checks that dtc-target-netinfo has been run and that the parameter file /etc/SFTKdtc_rootvg_failover_network_parms.txt exists; if not, just exit
- A message is displayed asking the user to make sure that the target bootlist has a safe maintenance-mode boot volume, in case some error would occur
- dtcfailover checks that we are replicating a LUN (hdiskx)
- If there is more than one device pair in the group, we log a warning that we expect the first pair to be the rootvg replication (needed in certain parts of the sequence)
- If a pre-failover script exists for this group, we run it (dtc_pre_failover_pxxx.sh)
- dtcfailover creates a marker file to disable replicator services: SFTKdtc_services_disabled
- log a message in dtcerror.log to indicate the cutoff point between the source server log and the target server log, because dtcerror.log is replicated to the target failover root drive and will be inherited and used after switch over by the target server, and hence the file will contain source server messages up to this point, and target server messages after that.
- dtcfailover stops the PMD of the failover replication group: killpmds -<group_number>; from this point on, nothing gets replicated anymore to the target failover boot volume
- dtcfailover removes the flag file on the source server: /etc/SFTKdtc_call_mktcpip_at_boot
- dtcfailover restores the original rc.tcpip on the source machine. This is done by editing (sed) the modified file to remove our modifications.
- If a post-failover script exists for this group, we run it (dtc_post_failover_pxxx.sh)
- Dtcfailover sends the command to the target server to complete the failover sequence. Note that in the case of the AIX rootvg failover, the command dtcsendfailover will not wait for a response from the target side, because the target server is rebooted and that may prevent it from sending any acknowledge.
- NOTE: the -s option (request to shutdown the source server) is not supported on AIX, since we stop the replication group PMD in order to restore the source rc.tcpip and remove the flag file /etc/SFTKdtc_call_mktcpip_at_boot without having this replicated to the target.

## 2.3 Target server part of the failover or scenario 2 (losing source server)

Our scripts on the target server do the following:
- Ensure journals application and disable the RMD of this group (run dtcrmdreco)
- If a post-failover script exists for this group, run it (dtc_post_failover_sxxx.sh)
- Identify the new boot disk from the RMD config file, then change the bootlist to boot from it (this is why we expect the rootvg pair to be the first one in the configuration file)
- Reboot from replicated rootvg hdisk.
- At reboot, the modified rc.tcpip calls our script: /etc/SFTKdtc_AIX_failover_boot_network_reconfig.sh, which does the following:
  - Check if the flag file /etc/SFTKdtc_call_mktcpip_at_boot exists; if not, just exit.
  - Read the network configuration parameter file created by dtc-target-netinfo (created on the source server and replicated to the target server); if the file is not found, exit.
  - Check which hdisk we are booting from (bootlist). If it matches the source server hdisk as defined in the group configuration file AND if the SFTKdtc-services-disabled flag is not found, it may mean that we are on the SOURCE server and that it has been rebooted from some reason. Just exit, then.
  - Remove the flag file /etc/SFTKdtc_call_mktcpip_at_boot
  - Reconfigure the network:
# 5) Remove network adapter devices:
/usr/sbin/lsdev -F name|/usr/bin/grep ent | /usr/bin/xargs -i -t /usr/sbin/rmdev -dl {} -R
# 6) Remove network adapter settings:
/usr/sbin/rmdev -dl $NetworkAdapter -R
# 7) Have AIX look for hardware/configuration (note: an error message is expected from cfgmgr, but it is to be ignored):
/usr/sbin/cfgmgr 2> /dev/null
# 8) Configure the network adapter again; here the mktcpip command arguments are taken from the user input from the parameter file generated by dtc-target-netinfo
/usr/bin/echo "SFTKdtc_AIX_failover_boot_network_reconfig.sh: reconfiguring network parameters with the following command:"
/usr/bin/echo "/usr/sbin/mktcpip -h $TargetHostname -a $TargetHostIPaddress -m $Subnetmask -i $NetworkInterface -n $NameServerIPaddress -d $DomainName -g $GatewayIPaddress -C $Cost -A $ActiveDeadGatewayDetection -t $CableType"
/usr/sbin/mktcpip -h $TargetHostname -a $TargetHostIPaddress -m $Subnetmask -i $NetworkInterface -n $NameServerIPaddress -d $DomainName -g $GatewayIPaddress -C $Cost -A $ActiveDeadGatewayDetection -t $CableType

- Rename all the replicator group configuration files and .cur files that were replicated from the source server, so that nobody can attempt to start a group defined for the source server and whose config files have been inherited on the target. The files are renamed with a suffix identifying the source server from which they have been replicated. Example:
  -rw-r--r-- 1 root system 918 Oct 10 11:28 p000.cfg.from_9.30.121.28
  -r--r----- 1 root system 918 Oct 10 12:36 p000.cur.from_9.30.121.28
- Complete the boot sequence.

## 2.4 Note on changing the bootlist to boot from a different disk

The command used by the script (automated) to switch the boot disk on the target at failover is bootlist.
For instance, if we switch to hdisk9, to change normal mode boot disk (multi-user mode):
bootlist -m normal hdisk9

In the target server failover messages log, you would see (assuming the new boot drive is hdisk9) :
[2013/11/01 12:23:01] dtcfailover: Launching target server post-failover script /etc/dtc/lib/dtc_post_failover_s000.sh
[2013/11/01 12:23:01] dtcfailover: The bootlist has been changed for booting from drive hdisk9.
[2013/11/01 12:23:01] dtcfailover: Failover sequence completed. Will now reboot from migrated boot drive.

If, for some reason, the configuration file is incorrect and and the new boot drive is not found, you would see error messages and instructions such as:

[2013/11/01 13:59:40] dtcfailover: Launching target server post-failover script /etc/dtc/lib/dtc_post_failover_s000.sh
[2013/11/01 15:01:04] dtcfailover: ERROR: did not find the hdisk device to failover to. Please verify the group configuration.
[2013/11/01 15:01:04] dtcfailover: Deleting the /etc/dtc/lib/s000.off flag file so that the PMD-RMD of this group can be launched again.
[2013/11/01 15:01:04] dtcfailover: IMPORTANT: after fixing the error situation, you must manually delete the /etc/dtc/lib/SFTKdtc_services_disabled flag file on the source server.
[2013/11/01 15:01:04] dtcfailover: Then you must rerun dtc-target-netinfo and launchpmds for this group to go back to Normal mode before relaunching dtcfailover.
[2013/11/01 15:01:04] dtcfailover: An error occured while attempting to change the bootlist. Exiting.
[2013/11/01 15:01:04] [proc: /usr/dtc/bin/in.dtc] [pid,ppid: 602280, 389354] [src,line: ftdd.c, 747] DTC: [FATAL / TARGET_FO_ERR]: Target failover of group 0 reported an error: rc = 256.

Also, if an hdisk is properly defined in the configuration file but the actual hdisk does not contain a valid blv (boot logical volume), you will see messages such as:

[2013/11/04 09:37:45] dtcfailover: Launching target server post-failover script /etc/dtc/lib/dtc_post_failover_s000.sh
[2013/11/04 09:37:46] dtcfailover: Original boot drive: hdisk0. New boot drive: hdisk9
[2013/11/04 09:37:46] dtcfailover: ERROR: the replicated boot drive hdisk9 does not seem to contain a boot logical volume.
[2013/11/04 09:54:06] dtcfailover: Please verify PMD-RMD configurations, bootlist, and error logs in /var/dtc/dtcerror.log.
[2013/11/04 09:37:46] dtcfailover: Restoring the original bootlist.
[2013/11/04 09:37:46] dtcfailover: Deleting the /etc/dtc/lib/s000.off flag file so that the PMD-RMD of this group can be launched again.
[2013/11/04 09:37:46] dtcfailover: IMPORTANT: after fixing the error situation, you must manually delete the /etc/dtc/lib/SFTKdtc_services_disabled flag file on the source server.
[2013/11/04 09:37:46] dtcfailover: Then you must rerun dtc-target-netinfo and launchpmds for this group to go back to Normal mode before relaunching dtcfailover.
[2013/11/04 09:37:46] dtcfailover: An error occured while attempting to change the bootlist. Exiting.
[2013/11/04 09:37:46] [proc: /usr/dtc/bin/in.dtc] [pid,ppid: 577694, 389354] [src,line: ftdd.c, 747] DTC: [FATAL / TARGET_FO_ERR]: Target failover of group 0 reported an error: rc = 256.

If it is at reboot from the new boot drive that the source hdisk is not found in the configuration file (while checking if we really are the target server, not the source), the script to reconfigure the network will exit with success status to avoid disrupting the boot sequence, and will not change the network parameters, but will log messages in the boot messages:

<<<<< SFTKdtc network reconfiguration at root drive failover on target server >>>>>
SFTKdtc_AIX_failover_boot_network_reconfig.sh: did not find an hdisk source device in the configuration file p000.cfg.
Please verify the configuration file.

Examples of manual usage of the bootlist command:
# bootlist -m normal -o
hdisk9 blv=hd5
The keyword for maintenance mode is “service”. To check the maintenance (single-user) mode boot disk, for instance:
# bootlist -m service -o
hdisk0 blv=hd5

To list the disks and see which one has the rootvg:
bash-3.2# lspv
hdisk0 00cd57de899abd23 rootvg active
hdisk1 none None
hdisk2 none None
hdisk3 00cd57de496c4164 VeritasVolumes
hdisk4 none VeritasVolumes
hdisk5 00cd57de496bbf5c VeritasVolumes
hdisk6 none VeritasVolumes
hdisk7 00cd57dee2c97379 vg01 active
hdisk8 none None
hdisk9 00cd57dee2c99bbd None
hdisk10 00cd57dee2c9a084 None

## 2.5 Location of failover control files

Various control files used for failover are stored in /etc, because all the files there are replicated to the target server and are visible upon switching to the new rootvg on the target at failover.
The main files are the following:

-rwxrwxr-- 1 root system 6511 Dec 18 14:43 rc.tcpip.preSFTKdtc
-rwxrwxrwx 1 bin bin 10190 Dec 20 12:28 SFTKdtc_AIX_failover_boot_network_reconfig.sh
-rwxrwxr-- 1 root system 6722 Dec 20 12:32 rc.tcpip
-rw-r--r-- 1 root system 283 Dec 20 12:32 SFTKdtc_rootvg_failover_network_parms.txt
-rw-r--r-- 1 root system 0 Dec 20 12:32 SFTKdtc_call_mktcpip_at_boot

All the files are cleaned up at package uninstall.

## 2.6 Example of configuration file used for testing

In this case, hdisk0 (rootvg) of the source server was replicated to the target server hdisk9, which became the new target rootvg at failover.

#===============================================================
# Softek Replicator Configuration File: /etc/dtc/lib/p000.cfg
# Softek Replicator Test Framework
#
# Last Updated: Wed Aug 28 12:35:41 2013
#===============================================================
#
# Primary System Definition:
#
SYSTEM-TAG: SYSTEM-A PRIMARY
HOST: 9.30.121.28
PSTORE: /dev/jfs2xx3
  DYNAMIC-ACTIVATION: on

#
# Secondary System Definition:
#
SYSTEM-TAG: SYSTEM-B SECONDARY
HOST: 9.30.121.29
JOURNAL: /journal

#
#
# Device Definitions:
#
PROFILE: 0
PRIMARY: SYSTEM-A
DTC-DEVICE: /dev/dtc/lg0/rdsk/dtc0
DATA-DISK: /dev/rhdisk0
SECONDARY: SYSTEM-B
MIRROR-DISK: /dev/rhdisk9
MIRROR-DEVNO: 1 46
#
#
# -- End of dtc Configuration File: /etc/opt/SFTKdtc/p000.cfg

## 2.7 If error upon stopping the PMD-RMD

If error when stopping PMD-RMD, we cleanup the SFTKdtc_call_mktcpip_at_boot flag file and restore the rc.tcpip script, and then we exit.

[2013/11/04 14:09:12] dtcfailover: Stopping the PMD and RMD of group 0...
[2013/11/04 14:09:13] dtcfailover: Error reported when stopping PMD/RMD (1); exiting failover sequence.
[2013/11/04 14:09:13] dtcfailover: Deleting the SFTKdtc_call_mktcpip_at_boot flag file and restoring original rc.tcpip
[2013/11/04 14:09:13] dtcfailover: The call to SFKTdtc failover network reconfiguration script was successfully removed from rc.tcpip

## 2.8 If error upon restoring rc.tcpip

If error when restoring rc.tcpip, we keep the modified rc.tcpip, but this will not cause problems because the SFTKdtc_call_mktcpip_at_boot flag file has been deleted. You will see messages such as:

[2013/11/04 16:21:57] dtcfailover: Stopping the PMD and RMD of group 0...
[2013/11/04 16:21:58] dtcfailover: Deleting the SFTKdtc_call_mktcpip_at_boot flag file and restoring original rc.tcpip.
[2013/11/04 16:21:58] dtcfailover: Copying /etc/rc.tcpip to /etc/rc.tcpip.postSFTKdtc failed.
[2013/11/04 16:21:58] dtcfailover: This error is most likely caused by directory permissions
[2013/11/04 16:21:58] dtcfailover: or being out of space on the filesystem assoicated with the
[2013/11/04 16:21:58] dtcfailover: /etc directory which is normally the root filesystem.
[2013/11/04 16:21:59] dtcfailover: Keeping the modified rc.tcpip but this will not cause problems since the flag file SFTKdtc_call_mktcpip_at_boot has been removed.
[2013/11/04 16:21:59] dtcfailover: Launching source server post-failover script /etc/dtc/lib/dtc_post_failover_p000.sh
[2013/11/04 16:21:59] dtcfailover: Source post-failover script for group 0 returned success status; continuing....
[2013/11/04 16:21:59] dtcfailover: Transferring rest of failover sequence to the target server...
[2013/11/04 16:21:59] dtcfailover: Transferred rest of failover sequence to the target server.

## 2.9 Note on testing

NOTE: the current testing is not representative of a real DR setup, because the LPARs are on the same physical machine. Testing will be required with 2 physical machines, or LPARS residing on different machines.

# 3. Procedure

- Install the product.
- Take note of the target server network configuration parameters from the most recent /smit.log mktcpip entry (on the target server, grep mktcpip /smit.log and take the most recent). The parameters that you need are the following:
  - Target server hostname
  - Target host IP address
  - Subnetmask
  - Network interface (e.g. en0)
  - NameServer IP address
  - Domain name (e.g. svl.ibm.com)
  - Default Gateway IP address
  - Cost for default route (-C arg to mktcpip, set to 0)
  - Do active dead gateway detection on default route? (-A arg to mktcpip, yes or no)
  - CableType (-t arg to mktcpip, can be N/A)
You also need to identify:
  - Network adapter (ex.: inet0)
  - Replication group number

- Configure the replication group that will be used for replicating the source rootvg to a target hdisk.
- Run dtc-target-netinfo and enter the network parameters of the target server, plus the replication group number.
- Start the replication group and do a Full Refresh.
- Once ready to launch the failover from the source server, you can monitor messages on the source and on the target with the command: tail -f /var/dtc/dtcerror.log.
- As long as the group is in Normal mode, the failover sequence can be launched from the source server with the command:
  - dtcfailover -g0 -b
- If you lose the source server and need to initiate a failover from the target server itself, the command to run is:
  - dtcfailover -g0 -b -r
- At the end of the sequence, the target will reboot from the new (replicated) rootvg.
- NOTE: a manual administration intervention may be needed on the target server after failover, because at this stage, after the sequence, the target sees its hdisks renumbered. Investigation on this is not yet completed in order to determine if this intervention can be automated in the scripts.

# 4. Post-failover state on source server

If we consider a case where the source server uses group 0 for the rootvg replication and failover and has some other replication groups not involved in the failover operation, such as a loopback group (group 1), after failover, the source server is the following state:

- source Agent state: running
- Source Groups' state:
0: Tracking
1: Normal

If we attempt to launchpmds on group 0, it is rejected. So, group 0 is kept in Tracking mode but we do not want it to replicate to the target anymore.
[2013/11/13 16:22:36] [proc: PMD_000] [pid,ppid: 581764, 397366] [src,line: pmd.c, 359] DTC: [INFO / SFTK_DISABLED]: SFTKdtc PMD launches have been disabled by marker file /etc/dtc/lib/SFTKdtc_services_disabled (dtcfailover sequence). Exiting.

If it is needed to relaunch group 0 and redo the sequence, then the flag file /etc/dtc/lib/SFTKdtc_services_disabled must be manually deleted first.

If the source is rebooted in this state, the Agent (in.dua) is relaunched.
Driver state: loaded, and the groups that were previously running are started in Tracking mode.
bash-3.2# dtcinfo -a | grep Mode
    Mode of operations.............. Tracking
    Mode of operations.............. Tracking

Messages at boot up:
[2013/11/29 13:38:31] FTD: /etc/dtc/init.d/dtc-startdriver: presence of file /etc/dtc/lib/SFTKdtc_services_disabled detected. The groups that were previously started will be placed in Tracking mode.
[2013/11/29 13:38:31] FTD: /etc/dtc/init.d/dtc-startdriver: if you want to restart replication groups PMDs on this server, you must run dtcstop for the group that was used for failover.
[2013/11/29 13:38:31] FTD: /etc/dtc/init.d/dtc-startdriver: then you must rename the configuration file pxxx.cfg of the group that was used for failover, ex.: rename to pxxx.cfg.for_failover, to prevent it from starting.
[2013/11/29 13:38:31] FTD: /etc/dtc/init.d/dtc-startdriver: after that, you can delete the file /etc/dtc/lib/SFTKdtc_services_disabled and start the desired replication groups PMDs, i.e. launchpmds.

Doing that procedure:
bash-3.2# dtcstop -g0
bash-3.2# mv p000.cfg p000.cfg.for_failover
bash-3.2# rm -f SFTKdtc_services_disabled
bash-3.2# launchpmds -g1
+- 13:48:21 -+- Logical Group 001 ----------------------------------------------------------+
| NORMAL | 0 KB 0 KB 0 KB 0 KB 0 0% |
| dtc1 0.00| 0.00 KB 0.00 KB 0.00 KB 0.00 KB 0 0.00% |

# 5. Losing the source server and initiating failover on the target

As described previously, if the source server was lost while in Normal mode and after
dtc-target-netinfo had been run (everything ready for failover), then you can initiate the failover on the target server side.
The command do so is the following:
ON TARGET SERVER:
dtcfailover -g0 -b -r
Note: -r is IMPORTANT (run target part only).
bash-3.2# dtcfailover -g0 -b -r
[2013/10/16 12:37:45] dtcfailover: Group 0 is in a 1-to-1 configuration on this server, RMD side.
[2013/10/16 12:37:45] dtcfailover: Target Server part of Failover started for group 0; command arguments: -g0 -b -r.
[2013/10/16 12:37:45] dtcfailover: Calling /usr/dtc/bin/dtcrmdreco to apply all Journals for group 0...
[2013/10/16 12:37:46] dtcfailover: The bootlist has been changed for booting from drive hdisk9.
[2013/10/16 12:37:46] dtcfailover: Failover sequence completed. Will now reboot from migrated boot drive.

BOOT MESSAGES (note: boot messages are the same when failover is initiated from the source server):

Starting tcpip daemons:
<<<<< SFTKdtc network reconfiguration at root drive failover on target server >>>>>
/usr/sbin/rmdev -dl ent0 -R
ent0 deleted
/usr/sbin/rmdev -dl ent1 -R
ent1 deleted
en0 deleted
et0 deleted
lo0 deleted
en1 deleted
et1 deleted
inet0 deleted
SFTKdtc_AIX_failover_boot_network_reconfig.sh: reconfiguring network parameters with the following command:
/usr/sbin/mktcpip -h sjpwr7ded -a 9.30.121.29 -m 255.255.255.0 -i en0 -n 9.0.128.50 -d svl.ibm.com -g 9.30.121.1 -C 0 -A no -t N/A
en0
sjpwr7ded
inet0 changed
en0 changed
inet0 changed
Renaming replicated source server /etc/dtc/lib/p000.cfg to /etc/dtc/lib/p000.cfg.from_9.30.121.28
Renaming replicated source server /etc/dtc/lib/p000.cur to /etc/dtc/lib/p000.cur.from_9.30.121.28
…

NOTE: after failover boot from the new boot disk, the new boot drive has the modified rc.tcpip script but it has no impact because the flag file SFTKdtc_call_mktcpip_at_boot has been deleted at the first reboot. The original rc.tcpip will be resotred at Replicator uninstall.

# 6. User pre/post failover scripts

As described in the design document on Generic Failover, similar to our pre-checkpoint and post-checkpoint scripts, we provide empty pre-failover and post-failover scripts with predefined paths to locate them (same location as the group configuration files) for the source server and a post-failover script for the target server.
These scripts have the names dtc_pre_failover_pxxx.sh and dtc_post_failover_pxxx.sh (where xxx must be changed to the actual 3-digit group number) on the primary (source) server, and dtc_post_failover_sxxx.sh on the secondary (target) server.

In order to use any of these scripts, they must be edited on site to contain the actual instructions they must execute, and the “xxx” part of their names must be replaced by the actual 3-digit group number for which they are intended to be used.
At installation, these scripts contain only one instruction, which is to exit with error status. If they are found, and then invoked, without being edited, the sequence will error out.
It is not mandatory to use any of the pre and post scripts. Also, for instance, if the user wants to use only the pre-failover script, he just needs to prepare only this script.

If an error is reported by the source server pre-failover script, the sequence aborts. At this stage of the process, all that needs to be done is to fix the user script and relaunch the failover.

If an error is reported by the source post-failover script, however, then, in addition to fixing the script, dtc-target-netinfo must be run again and the PMD must be relaunched prior to restarting the failover. You would see messages such as:

[2013/10/29 14:02:37] dtcfailover: Creating marker file /etc/dtc/lib/SFTKdtc_services_disabled to deactivate SFTKdtc services after failover to new boot drive.
[2013/10/29 14:02:37] dtcfailover: Stopping the PMD and RMD of group 0...
[2013/10/29 14:02:38] dtcfailover: Deleting the SFTKdtc_call_mktcpip_at_boot flag file and restoring original rc.tcpip
[2013/10/29 14:02:38] dtcfailover: The call to SFKTdtc failover network reconfiguration script was successfully removed from rc.tcpip
[2013/10/29 14:02:39] dtcfailover: Launching source server post-failover script /etc/dtc/lib/dtc_post_failover_p000.sh
[2013/10/29 14:02:39] dtcfailover: Post-failover script /etc/dtc/lib/dtc_post_failover_p000.sh returned error code 1; exiting failover sequence.
[2013/10/29 14:02:39] dtcfailover: Deleting the /etc/dtc/lib/SFTKdtc_services_disabled flag file so that the PMD can be launched again.
[2013/10/29 14:02:39] dtcfailover: IMPORTANT: after fixing the error situation with the script /etc/dtc/lib/dtc_post_failover_p000.sh, you must rerun dtc-target-netinfo
[2013/10/29 14:02:39] dtcfailover: and launchpmds for this group to go back to Normal mode before relaunching dtcfailover.

If the error is with the target server post-failover script, you get the following messages:

[2013/10/31 15:13:53] dtcfailover: Launching target server post-failover script /etc/dtc/lib/dtc_post_failover_s000.sh
[2013/10/31 15:13:53] dtcfailover: Post-failover script /etc/dtc/lib/dtc_post_failover_s000.sh returned error code 1; exiting failover sequence.
[2013/10/31 15:13:53] dtcfailover: Deleting the /etc/dtc/lib/sxxx.off flag file so that the PMD-RMD of this group can be launched again.
[2013/10/31 15:13:53] dtcfailover: IMPORTANT: after fixing the error situation with the script /etc/dtc/lib/dtc_post_failover_s000.sh, you must manually delete
[2013/10/31 15:13:53] dtcfailover: the /etc/dtc/lib/SFTKdtc_services_disabled flag file on the source server, rerun dtc-target-netinfo
[2013/10/31 15:13:53] dtcfailover: and launchpmds for this group to go back to Normal mode before relaunching dtcfailover.

# 7. What if the source server is rebooted before failover

If the source server is rebooted after dtc-target-netinfo has been run, which implies that it has a modified /etc/rc.tcpip with an instruction inserted to call our network reconfiguration at boot time, you should see boot messages such as:
<<<<< SFTKdtc network reconfiguration at root drive failover on target server >>>>>
SFTKdtc_AIX_failover_boot_network_reconfig.sh:
The failover flag file /etc/dtc/lib/SFTKdtc_services_disabled has not been found. This indicates that the source server was rebooted
or crashed outside the context of a normal failover operation. Also, the current bootdrive is the same as the source hdisk identified
in the configuration file /etc/dtc/lib/p000.cfg (/dev/rhdisk0), so we are not changing the network configuration.

There can be re-entries in rc.tcpip, so you can see this message more than once. As the message says, our script detects that it is running on the source server and does not reconfigure the network.

# 8. hdisks renumbered

One aspect which has not been sorted out yet is that after failover boot on the target server, the hdisks get renumbered. So, in the example where we replicate the source server hdisk0 to the target server hdisk9 and make it the new target boot disk, hdisk9 is seen as hdisk20.

Target server before failover:
bash-3.2# lspv
hdisk0 00cd57de899abd23 rootvg active
hdisk1 none None
hdisk2 none None
hdisk3 00cd57de496c4164 VeritasVolumes
hdisk4 none VeritasVolumes
hdisk5 00cd57de496bbf5c VeritasVolumes
hdisk6 none VeritasVolumes
hdisk7 00cd57dee2c97379 vg01 active
hdisk8 none None
hdisk9 00cd57dee2c99bbd None
hdisk10 00cd57dee2c9a084 None

bash-3.2# lsdev -Ccdisk
hdisk0 Available 05-08-00-8,0 16 Bit LVD SCSI Disk Drive
hdisk1 Available 05-08-00-9,0 16 Bit LVD SCSI Disk Drive
hdisk2 Available 05-08-00-10,0 16 Bit LVD SCSI Disk Drive
hdisk3 Available 03-08-02 MPIO Other FC SCSI Disk Drive
hdisk4 Available 03-08-02 MPIO Other FC SCSI Disk Drive
hdisk5 Available 03-08-02 MPIO Other FC SCSI Disk Drive
hdisk6 Available 03-08-02 MPIO Other FC SCSI Disk Drive
hdisk7 Available 03-08-02 MPIO Other FC SCSI Disk Drive
hdisk8 Available 03-08-02 MPIO Other FC SCSI Disk Drive
hdisk9 Available 03-08-02 MPIO Other FC SCSI Disk Drive
hdisk10 Available 03-08-02 MPIO Other FC SCSI Disk Drive

Replicating Source server hdisk0 to Target server hdisk9, then doing the failover, which changes the bootlist to hdisk9 on the target and reboots.
Now, after failover, the target server has the hdisks renumbered:
bash-3.2# lspv
hdisk11 00cd57de899abd23 None
hdisk12 none None
hdisk13 none None
hdisk14 00cd57de496c4164 None
hdisk15 none None
hdisk16 00cd57de496bbf5c None
hdisk17 none None
hdisk18 00cd57dee2c97379 None
hdisk19 none None
hdisk20 00cd57de57242b55 rootvg active
hdisk21 00cd57dee2c9a084 None

bash-3.2# lsdev -Ccdisk
hdisk0 Defined 05-08-00-8,0 16 Bit LVD SCSI Disk Drive
hdisk1 Defined 05-08-00-9,0 16 Bit LVD SCSI Disk Drive
hdisk2 Defined 05-08-00-10,0 16 Bit LVD SCSI Disk Drive
hdisk3 Defined 03-08-02 MPIO Other FC SCSI Disk Drive
hdisk4 Defined 03-08-02 MPIO Other FC SCSI Disk Drive
hdisk5 Defined 03-08-02 MPIO Other FC SCSI Disk Drive
hdisk6 Defined 03-08-02 MPIO Other FC SCSI Disk Drive
hdisk7 Defined 03-08-02 MPIO Other FC SCSI Disk Drive
hdisk8 Defined 03-08-02 MPIO Other FC SCSI Disk Drive
hdisk9 Defined 03-08-02 MPIO Other FC SCSI Disk Drive
hdisk10 Defined 03-08-02 MPIO Other FC SCSI Disk Drive
hdisk11 Available 0B-08-00-8,0 16 Bit LVD SCSI Disk Drive
hdisk12 Available 0B-08-00-9,0 16 Bit LVD SCSI Disk Drive
hdisk13 Available 0B-08-00-10,0 16 Bit LVD SCSI Disk Drive
hdisk14 Available 09-08-02 MPIO Other FC SCSI Disk Drive
hdisk15 Available 09-08-02 MPIO Other FC SCSI Disk Drive
hdisk16 Available 09-08-02 MPIO Other FC SCSI Disk Drive
hdisk17 Available 09-08-02 MPIO Other FC SCSI Disk Drive
hdisk18 Available 09-08-02 MPIO Other FC SCSI Disk Drive
hdisk19 Available 09-08-02 MPIO Other FC SCSI Disk Drive
hdisk20 Available 09-08-02 MPIO Other FC SCSI Disk Drive
hdisk21 Available 09-08-02 MPIO Other FC SCSI Disk Drive

bash-3.2# bootlist -m normal -o
hdisk20 blv=hd5

A manual administration intervention may be needed on the target server after failover, because at this stage, after the sequence, the target sees its hdisks renumbered. Investigation on this is not yet completed in order to determine if this intervention can be automated in the scripts.

An attempt at removing all the “Defined” hdisks and running cfgmgr (and even rebooting) did not fix this.

rmdev -dl hdisk0 to hdisk10
bash-3.2# rmdev -dl hdisk0
hdisk0 deleted
bash-3.2# rmdev -dl hdisk1
hdisk1 deleted
etc... up to hdisk10
bash-3.2# rmdev -dl hdisk10
hdisk10 deleted

bash-3.2# lsdev -Ccdisk
hdisk11 Available 0B-08-00-8,0 16 Bit LVD SCSI Disk Drive
hdisk12 Available 0B-08-00-9,0 16 Bit LVD SCSI Disk Drive
hdisk13 Available 0B-08-00-10,0 16 Bit LVD SCSI Disk Drive
hdisk14 Available 09-08-02 MPIO Other FC SCSI Disk Drive
hdisk15 Available 09-08-02 MPIO Other FC SCSI Disk Drive
hdisk16 Available 09-08-02 MPIO Other FC SCSI Disk Drive
hdisk17 Available 09-08-02 MPIO Other FC SCSI Disk Drive
hdisk18 Available 09-08-02 MPIO Other FC SCSI Disk Drive
hdisk19 Available 09-08-02 MPIO Other FC SCSI Disk Drive
hdisk20 Available 09-08-02 MPIO Other FC SCSI Disk Drive
hdisk21 Available 09-08-02 MPIO Other FC SCSI Disk Drive

cfgmgr

Still hdisk11 to 21

# 9. debugcapture

On source server before failover, after dtc-target-netinfo, in Normal mode:

Test example:
sjpwr7dec.20131216-1209 debugcapture

in ./etc:
-rw-r--r-- 1 paulclou dms 10190 Nov 29 08:46 SFTKdtc_AIX_failover_boot_network_reconfig.sh
-rw-r--r-- 1 paulclou dms 6722 Dec 16 08:52 rc.tcpip
-rw-r--r-- 1 paulclou dms 283 Dec 16 08:52 SFTKdtc_rootvg_failover_network_parms.txt
-rw-r--r-- 1 paulclou dms 0 Dec 16 08:52 SFTKdtc_call_mktcpip_at_boot

bash-3.00$ diff rc.tcpip.preSFTKdtc rc.tcpip
44a45,47
> # @@@ CALL TO SFTKdtc FAILOVER NETWORK RECONFIGURATION SCRIPT + @@@
> /etc/SFTKdtc_AIX_failover_boot_network_reconfig.sh
> # @@@ CALL TO SFTKdtc FAILOVER NETWORK RECONFIGURATION SCRIPT - @@@

bash-3.00$ cat SFTKdtc_rootvg_failover_network_parms.txt
TargetHostname: sjpwr7ded
TargetHostIPaddress: 9.30.121.29
Subnetmask: 255.255.255.0
NetworkInterface: en0
NameServerIPaddress: 9.0.128.50
DomainName: svl.ibm.com
GatewayIPaddress: 9.30.121.1
Cost: 0
ActiveDeadGatewayDetection: no
CableType: N/A
NetworkAdapter: inet0
GroupNumber: 0

Flag file is there to call network reconfig script at failover boot on target.
rc.tcpip has the modification to call our network reconfig script.
Network parameter file is there.

On source server after failover:
Test example:
sjpwr7dec.20131216-1215 debugcapture

-rw-r--r-- 1 paulclou dms 10190 Nov 29 08:46 SFTKdtc_AIX_failover_boot_network_reconfig.sh
-rw-r--r-- 1 paulclou dms 6511 Dec 12 13:23 rc.tcpip.preSFTKdtc
-rw-r--r-- 1 paulclou dms 283 Dec 16 08:52 SFTKdtc_rootvg_failover_network_parms.txt
-rw-r--r-- 1 paulclou dms 6511 Dec 16 10:14 rc.tcpip

bash-3.00$ diff rc.tcpip rc.tcpip.preSFTKdtc
No diff: OK
Network parameters OK
Flag file to call our network reconfig script has been removed: OK

In ./etc/dtc/lib
-rw-r--r-- 1 paulclou dms 1298 Nov 29 08:46 dtc_pre_failover_pxxx.sh
-rw-r--r-- 1 paulclou dms 1491 Nov 29 08:46 dtc_pre_failover_p000.sh
-rw-r--r-- 1 paulclou dms 797 Nov 29 08:46 dtc_post_failover_sxxx.sh
-rw-r--r-- 1 paulclou dms 785 Nov 29 08:46 dtc_post_failover_pxxx.sh
-rw-r--r-- 1 paulclou dms 982 Nov 29 08:46 dtc_post_failover_p000.sh
-rw-r--r-- 1 paulclou dms 25 Nov 29 08:46 DTC.lic
-rw-r--r-- 1 paulclou dms 75 Nov 29 08:46 dtcAgent.cfg
-rw-r--r-- 1 paulclou dms 920 Nov 29 08:46 s001.cfg
-rw-r--r-- 1 paulclou dms 920 Nov 29 08:46 p001.cfg
-rw-r--r-- 1 paulclou dms 918 Nov 29 08:46 p000.cfg.for_failover
-rw-r--r-- 1 paulclou dms 918 Nov 29 08:46 p000.cfg
-rw-r--r-- 1 paulclou dms 918 Dec 16 08:55 p000.cur
-rw-r--r-- 1 paulclou dms 920 Dec 16 08:55 p001.cur
-rw-r--r-- 1 paulclou dms 0 Dec 16 10:14 SFTKdtc_services_disabled

On target if failover fails, still on original boot drive:
Using "dtc_post_failover_s000.sh" with exit 1 to simulate the error.
[2013/12/16 12:14:17] dtcfailover: Launching target server post-failover script /etc/dtc/lib/dtc_post_failover_s000.sh
[2013/12/16 12:14:17] dtcfailover: Post-failover script /etc/dtc/lib/dtc_post_failover_s000.sh returned error code 1; exiting failover sequence.
[2013/12/16 12:14:17] dtcfailover: Deleting the /etc/dtc/lib/s000.off flag file so that the PMD-RMD of this group can be launched again.
[2013/12/16 12:14:17] dtcfailover: IMPORTANT: after fixing the error situation with the script /etc/dtc/lib/dtc_post_failover_s000.sh, you must manually delete the /etc/dtc/lib/SFTKdtc_services_disabled flag file on the source server.
[2013/12/16 12:14:17] dtcfailover: Then you must rerun dtc-target-netinfo and launchpmds for this group to go back to Normal mode before relaunching dtcfailover.
[2013/12/16 12:14:17] [proc: /usr/dtc/bin/in.dtc] [pid,ppid: 602254, 393226] [src,line: ftdd.c, 747] DTC: [FATAL / TARGET_FO_ERR]: Target failover of group 0 reported an error: rc = 256.

In the test debugcapture file sjpwr7ded.20131216-1217
We have ./var/dtc/dtcerror.log with the above messages.

On target after booting from new boot drive:

In the test debugcapture file sjpwr7ded.20131216-1241:

-rw-r--r-- 1 paulclou dms 10190 Nov 29 08:46 SFTKdtc_AIX_failover_boot_network_reconfig.sh
-rw-r--r-- 1 paulclou dms 344872 Nov 29 08:46 services
-rw-r--r-- 1 paulclou dms 3051 Nov 29 08:46 rc
-rw-r--r-- 1 paulclou dms 6511 Dec 16 10:14 rc.tcpip.preSFTKdtc
-rw-r--r-- 1 paulclou dms 283 Dec 16 10:32 SFTKdtc_rootvg_failover_network_parms.txt
-rw-r--r-- 1 paulclou dms 6722 Dec 16 10:32 rc.tcpip

bash-3.00$ diff rc.tcpip rc.tcpip.preSFTKdtc
45,47d44
< # @@@ CALL TO SFTKdtc FAILOVER NETWORK RECONFIGURATION SCRIPT + @@@
< /etc/SFTKdtc_AIX_failover_boot_network_reconfig.sh
< # @@@ CALL TO SFTKdtc FAILOVER NETWORK RECONFIGURATION SCRIPT - @@@

It has the modified rc.tcpip but the flag file has been removed so it is OK; won't have any effect as the network reconfig script will just exit. And the original rc.tcpip is restored at replicator uninstall.

As mentionned previously, dtcerror.log has part of the source log up to failover killpmds on source and then the logged messages are from the target at boot time, since it inherits from the replicated dtcerror.log and takes over with it. A cut-off point message is logged to indicate that.
Example:
[2013/12/18 13:12:39] dtcfailover: Creating marker file /etc/dtc/lib/SFTKdtc_services_disabled to deactivate SFTKdtc services after failover to new boot drive.
[2013/12/18 13:12:39] dtcfailover: NOTE: preceding log entries are from the source server sjpwr7dec.svl.ibm.com (message intended to target server to which this logfile is replicated).
[2013/12/18 13:17:16] FTD: /etc/dtc/init.d/dtc-startdriver: presence of file /etc/dtc/lib/SFTKdtc_services_disabled detected. The groups that were previously started will be placed in Tracking mode.
[2013/12/18 13:17:16] FTD: /etc/dtc/init.d/dtc-startdriver: if you want to restart replication groups PMDs on this server, you must run dtcstop for the group that was used for failover.

The boot messages are also available in the debugcapture.
Example after a test:
 /var/tmp/sjpwr7ded.20131112-1051.tar.Z
We have our messages in the alog -o -t console section:
        0 Tue Nov 12 09:59:24 CST 2013 <<<<< SFTKdtc network reconfiguration at root drive failover on target server >>>>>
        0 Tue Nov 12 09:59:24 CST 2013 /usr/sbin/rmdev 0 Tue Nov 12 09:59:24 CST 2013 0 Tue Nov 12 09:59:24 CST 2013 -dl 0 Tue Nov 12 09:59:24 CST 2013 0 Tue Nov 12 09:59:24 CST 2013 ent0 0 Tue Nov 12 09:59:24 CST 2013 0 Tue Nov 12 09:59:24 CST 2013 -R 0 Tue Nov 12 09:59:24 CST 2013 0 Tue Nov 12 09:59:24 CST 2013
        0 Tue Nov 12 09:59:24 CST 2013 ent0 deleted
        0 Tue Nov 12 09:59:24 CST 2013 /usr/sbin/rmdev 0 Tue Nov 12 09:59:24 CST 2013 0 Tue Nov 12 09:59:24 CST 2013 -dl 0 Tue Nov 12 09:59:24 CST 2013 0 Tue Nov 12 09:59:24 CST 2013 ent1 0 Tue Nov 12 09:59:24 CST 2013 0 Tue Nov 12 09:59:24 CST 2013 -R 0 Tue Nov 12 09:59:24 CST 2013 0 Tue Nov 12 09:59:24 CST 2013
        0 Tue Nov 12 09:59:24 CST 2013 ent1 deleted
        0 Tue Nov 12 09:59:24 CST 2013 en0 deleted
        0 Tue Nov 12 09:59:24 CST 2013 et0 deleted
        0 Tue Nov 12 09:59:24 CST 2013 lo0 deleted
        0 Tue Nov 12 09:59:24 CST 2013 en1 deleted
        0 Tue Nov 12 09:59:24 CST 2013 et1 deleted
        0 Tue Nov 12 09:59:24 CST 2013 inet0 deleted
        0 Tue Nov 12 09:59:56 CST 2013 SFTKdtc_AIX_failover_boot_network_reconfig.sh: reconfiguring network parameters with the following command:
        0 Tue Nov 12 09:59:56 CST 2013 /usr/sbin/mktcpip -h sjpwr7ded -a 9.30.121.29 -m 255.255.255.0 -i en0 -n 9.0.128.50 -d svl.ibm.com -g 9.30.121.1 -C 0 -A no -t N/A
        0 Tue Nov 12 09:59:56 CST 2013 en0
        0 Tue Nov 12 09:59:56 CST 2013 sjpwr7ded
        0 Tue Nov 12 09:59:56 CST 2013 inet0 changed
        0 Tue Nov 12 09:59:56 CST 2013 en0 changed
        0 Tue Nov 12 09:59:56 CST 2013 inet0 changed
        0 Tue Nov 12 09:59:56 CST 2013 Renaming replicated source server /etc/dtc/lib/p000.cfg to /etc/dtc/lib/p000.cfg.from_9.30.121.28
        0 Tue Nov 12 09:59:56 CST 2013 Renaming replicated source server /etc/dtc/lib/p000.cur to /etc/dtc/lib/p000.cur.from_9.30.121.28
        0 Tue Nov 12 10:00:01 CST 2013 0513-059 The syslogd Subsystem has been started. Subsystem PID is 299206.

# 10. Bad sector table

We must verify if the replication of the rootvg from a source to a target server must do special handling to preserve, on the target server disk, a bad sector table.
<<< still to be investigated
This would require a manual intervention, saving the bad sector table to a file on the target before Full Refreh.